## Slide 1: Introduction to Embedded C Programming.

## Slide 2: Introduction
Programming is the process of creating a set of instructions that tell a computer how to perform a task.
Programming can be done using a variety of computer programming languages, such as JavaScript, Python, C and C++.

## Slide 3: Embedded C programming
Embedded C is one of the most popular and most commonly used Programming Languages in the development of Embedded Systems.
An Embedded System is a system which has both the hardware and software and is designed to do a specific task.
Embedded Software or Program allow Hardware to monitor external events (Inputs) and control external devices (Outputs) accordingly.

## Slide 4: Embedded C programming cont…
A software program is written on a special IDE (Integrated Development Environment) on a computer and uploaded to the microcontroller for execution.
Embedded C is basically an extension to the Standard C Programming Language with additional features.
It uses the same syntax and semantics of the C Programming Language like main function, declaration of datatypes, defining variables, loops, functions, statements, etc.

## Slide 5: Parts of Arduino Program
Arduino program can be divided in three main parts;
values(variables and constants),
structure and
functions.

## Slide 7: Variables(constants & data types)
Constants
HIGH | LOW
INPUT | OUTPUT
true | false
integer constants
floating point constants, etc.

## Slide 8: Data types

## Slide 9: Some functions in Arduino program
pinMode()
It configures the specified pin to behave either as an input or an output. Eg. pinMode ( ledPin, OUTPUT);
digitalWrite()
Write a HIGH or a LOW value to a digital pin.
Eg. digitalWrite (ledPin, HIGH);
digitalRead()
Reads the value from a specified digital pin, either HIGH or LOW.
Eg. digitalRead(pin);

## Slide 10: Functions in Arduino program cont…
analogRead()
Reads the value from the specified analog pin.
eg. float value=analogRead (inPin);
analogWrite()
Writes an analog value (PWM wave) to a pin.
eg. analogWrite (ledPin, Value/4);

## Slide 11: Time functions
delay()
Pauses the program for the amount of time (in miliseconds) specified as parameter. (There are 1000 milliseconds in a second.)
eg. delay(1000);
delayMicrosecods()
Pauses the program for the amount of time (in microseconds) specified as parameter. There are million microseconds in a second.
eg. delayMicroseconds(10000)
Other time functions include; millis() and micros()

## Slide 12: Some control structures in Arduino program
If
if (conditional) and ==, !=, <, > (comparison operators)
If,is used in conjunction with a comparison operator, tests whether a certain condition has been reached, such as an input being above a certain number.
Syntax;
if (SensorValue<25) {
//do something
}

## Slide 13: Control structure cont…
If…else
if/else allows greater control over the flow of code than the basic if statement, by allowing multiple tests to be grouped together.
Syntax;
if (SensorValue<25) {
//Action A
}
else {
//Action B
}

## Slide 14: Control structure cont…
for statement
The for statement is used to repeat a block of statements enclosed in curly braces. An increment counter is usually used to increment and terminate the loop.

## Slide 15: Control structure cont…
while
while loops will loop continuously, and infinitely, until the expression inside the parenthesis, () becomes false.
Syntax;
while(expression){
//statement(s)
}

## Slide 16: Other control structures you need to know
switch case
do…while
break
continue
return
goto